세미나 자료 : Introduction to Remote Desktop protocol

2002-09-13, swkim@clunix.com

0. Background

- Based on ITU-T T-120 family

. Especially T.128 : Application Sharing

. Multichannel capable protocol : 64,000 separate channels for data transmission

. Multipoint data delivery in real-time

- supports ISDN, POTS, LAN(IPX, NetBIOS, TCP/IP…)

- Terminal service device driver

. wdtshare.sys : UI transfer, compression, encryption, framing…

. tdtcp.sys : transport driver. Package onto TCP/IP

1. Feature

- Encryption

. RSA Security’s RC4 cipher

. security setting

. low : password, etc.

. medium : 56-bit key bi-directionally encrypt

. 128-bit : require W2K High Encryption Pack

- Bandwidth Reduction

. compression

. bitmap caching (memory)

. persistent bitmap caching (disk) : to use with subsequent session

- Roaming Disconnect

. reconnect to disconnected session on different device

. resolution is automatically resized

- Clipboard Mapping

. cut/copy/paste test and graphics between local<->server, session<->session

- Print Redirection

. print to a printer attached to the client device

- Virtual Channels

. using the RDP Virtual Channel Architecture, new applications can be developed which uses terminal service session

- Remote Control

. authorized person can view or control another Terminal Service session

- Network Load Balancing

. W2K Advanced Server의 NLB를 이용할 수도 있다…